## Slide 1: EEG-Based Brain Activity Detection to Indian Classical Music
A Review of: Real-time Measures for Brain Activity Detection to Live Indian Classical Music Stimulus

## Slide 2: Introduction
• Study of music's impact on the brain using EEG.
• Focus on Indian Classical Music (ICM), specifically Hindustani style.
• Measures brain response in real-time to live music performance.

## Slide 3: Motivation
• Music therapy has shown benefits for emotional and physical well-being.
• Existing studies lack real-time data and focus on recorded music.
• This study uses live music and advanced signal processing.

## Slide 4: What is EEG?
• Electroencephalography records electrical activity of the brain.
• Non-invasive electrodes placed on the scalp.
• Signals categorized into Delta, Theta, Alpha, Beta, Gamma bands.

## Slide 5: About Indian Classical Music
• Uses Swaras: Sa, Re, Ga, Ma, Pa, Dha, Ni.
• Includes natural (Suddh), flat (Komal), and sharp (Teevra) notes.
• Frequency varies by octave; musical structure called Raga.

## Slide 6: Ragas Used in Study
• Two Ragas: Yaman and Puria Dhanashree (PD).
• Difference lies in notes Re and Dha.
• Used to evaluate brain response to subtle musical variation.

## Slide 7: Volunteers & Setup
• 10 volunteers: some musically trained, others not.
• EEG cap with 24 channels used.
• Data recorded using CameraEEG app (500 Hz).

## Slide 8: Experimental Paradigm
• Live vocal performance: Initiation, Yaman, Relax, Transition to PD, PD, Final relax.
• Audio and EEG recorded simultaneously for synchronization.

## Slide 9: Preprocessing
• EEG data converted to .mat using EEGLAB.
• 4 brain regions analyzed: Frontal, Left/Right Temporal, Parieto-Occipital.
• No artifact removal to preserve authenticity.

## Slide 10: Mahalanobis Distance (MD)
• Measures deviation of brain response from average state.
• Formula: DM = √((Y − μ)ᵗ W⁻¹ (Y − μ))
• W: Covariance matrix, μ: mean vector.

## Slide 11: Recursive MD
• Allows real-time update of MD.
• Updates mean and covariance without recomputing all data.
• Useful for continuous EEG monitoring.

## Slide 12: Energy Measure
• Quantifies signal power in brain regions.
• Formula: E = (1/N) Σ(Yᵢ)²
• Higher energy = stronger brain activity.

## Slide 13: Recursive Energy Measure
• Updates energy in real-time with each new data point.
• Eₖ = ((k-1)/k)Eₖ + (1/k)(YₖYₖᵗ)
• Works well with MD for brain state tracking.

## Slide 14: Hilbert Transform & PDFs
• Used to extract instantaneous frequencies of swaras.
• PDFs show how note frequencies vary between ragas.

## Slide 15: EEG Topographic Plots
• Topo maps show spatial activation across brain for different notes.
• Varies by note, raga, and subject.
• Dynamic changes observed in alpha band.

## Slide 16: Energy Analysis (Bar Plots)
• Subject 1 (HCM trained): Parieto-Occipital active.
• Subject 4 (Carnatic): Right Temporal active.
• Others: Mixed response depending on raga.

## Slide 17: Recursive Energy (Transition)
• Monitored from Relax (225–229s) to Yaman (229–233s).
• Shows increased activity, especially in Parieto-Occipital region.

## Slide 18: Recursive MD (Validation)
• Confirms transition from relaxed to active state at 229s.
• Sudden spike in MD indicates brain shift due to music stimulus.

## Slide 19: Conclusion
• Different ragas activate different brain regions.
• Prior music training affects response.
• Recursive methods allow real-time tracking — useful for music therapy.

## Slide 20: What You Should Learn
• EEG basics and band interpretation.
• Recursive Mahalanobis Distance & Energy computation.
• How music affects cognition — potential for therapeutic applications.

## Slide 21: Acknowledgement & References
• Based on INDICON 2023 Paper
• Tools used: MATLAB, EEGLAB, CameraEEG
• Keywords: EEG, Mahalanobis Distance, Energy, Raga, Brain Response